## Slide 1: Use of SystemVerilog Interfaces in RTL Design and Test Benches A small example based on SPI
Dr. Mark C. Johnson
March, 2016
Notes: System Verilog interfaces are a feature that will help you to make your code much more modular and readable. In addition, in ECE437 you will be using SV interfaces frequently.
This module is designed on the assumption that you are at least somewhat familiar with the operation of an SPI (serial peripheral interface) bus. You don’t need to be expert on it, but if you aren’t familiar, you may find it helpful to find an explanation of SPI online before continuing with this module.

## Slide 2
SPI Interconnect without
using modular interface
definition.
Notes: I have chosen SPI as just about the simplest bus interface available. Even such a simple bus benefits from use of SV interfaces. This slide illustrates in a block diagram how, without interfaces, you have to explicitly declare and connect each wire of the bus individually. In Verilog it means having to list each element of the bus individually in your port maps.
The timing diagram at the bottom illustrates the operation of this SPI implementation. This SPI implementation is designed for each bit of serial input to be read and stored in a register on or shortly after the rising edge of SCK. Bits are transmitted in this design at least a half cycle of SCK before each rising edge of SCK and the bit value is held until the falling edge of SCK.
There are two slave select lines SS[0] and SS[1] used to individually tell each of two SPI slaves which is to be enabled for communication.
If you study the waveforms on this slide, you should observe the following sequence of events.
1. The master transmits the value 10001111 to slave 1. Slave 1 simultaneously transmits 11101010 back to the master
2. The master transmits 00110011 to slave 0. Slave 0 simultaneously transmits 110010111 to the master.
3. The master transmits 00100101 to slave 1. Slave 1 transmits 01001111.

## Slide 3
SPI Interconnect with modular interface
definition.
Notes: Compare this to the previous slide. The only difference in the diagram is that all of the wires that make up SPI are represented by a single bus and each master and slave device includes an interface, SPIbus, in it’s port map to be able to connect to the bus. You will soon see an example of what this looks like in code.
Notice that the master uses SPIbus.Master() rather than just SPIbus as the port. SV interfaces support a feature called modports which specify the direction of each wire in the bus (in or out). Similarly the slaves use SPIbus.Slave() where Slave() identifies the modport definition to be used by the slave. Hopefully, this will make more sense when you see the code examples.

## Slide 4
Organization of test bench using SV interfaces.
Notes: SV interfaces are useful for more than just interconnect between modules in your RTL design. They are also useful in making connections between your test bench stimulus/checker code and the modules to be tested.
When designing these modules and the test bench, I found that I needed the same set of control inputs to each module to monitor the values received on the SPI bus and to provide values to be transmitted. It cleaned up the code considerably when I defined a control bus, SPIctrl, to manage the communication between the test bench and the modules under test.

## Slide 5
Code to define interface, put in a header file
Notes: Now let’s see how this looks in code.
An SV interface is something you are likely to need to use in many different modules, so it is helpful to put the interface definition in a header file to be included later.
interface SPIbus declares the name of the interface
mosi, sck, miso, and ss (slave select) are all elements of the SPI bus
modport Master specifies which elements of the bus are inputs/outputs for any device that uses the modport Master
modport Slave specifies which elements of the bus are inputs/outputs for any device that uses the modport Master
The SPIctrl interface uses all the same syntax, but there is an additional modport called System intended for controlling an SPI master or slave. We will use the System modport in the test bench, but if you were building the SPI devices into a larger system, you would use SPIctrl.System() to connect the SPI device to other modules in your design.

## Slide 6
Use of interface in SPI master
commented out because already loaded elsewhere
Ctrl is an instance of SPIctrl with input/output as given by
master modport. Spim is an instance of SPIbus with Master modport
References to elements
of Ctrl interface as inputs
Notes: Here are examples of how the SPIbus and SPIctrl interfaces can be used in the RTL code for your SPI master.
If this module is the first place in the code for you system where these busses are used, you will need an include statement to pull in the interface definition header file. In this case, the include statement is commented out because the header file is included in the test bench.
The port list for the module master specifies modport SPIctrl.Master as the first port and assigns it the name Ctrl as the name to be used inside the module. If you look at the code fragment further down, Ctrl.ss and Ctrl.toXmit are used as inputs in the code.
SPIbus.Master is assigned to the name Spim for use in the master module, but the code fragment below does not use it.

## Slide 7
Use of interface in SPI master
assign values to elements
of an interface as outputs
Notes: Interfaces can be used both in dataflow and behavioral code. Here, dataflow statements are used to assign values to outputs Spim.mosi, Spim.sck, and Spim.ss.
The code further down assigns output values to Ctrl.busy. This is a notification to the external system or test bench that the SPI master is busy and unable to accept any new values to be transmitted.

## Slide 8
Use of interface in SPI slave
Very similar to interface use in SPI master (examples)
Notes: Here are examples of how the SPIbus and SPIctrl interfaces are used in the SPI slave. The syntax is exactly the same as what was used for the SPI master, but notice that this time different modports are used.

## Slide 9
Use of interface in test bench
In this lecture we will just focus on the
use of interfaces. In another lecture we
will look at many other aspects of the
test bench design such as random input
generation, use of assertions, etc.
Interfaces are used as a data type
For course code simulation, interfaces can be used as ports in and out
of the device under test. The modports (Slave, Master) are specified
since the modports define the direction of elements in the interface.
Notes: This and the next couple of slides are used to show how the interfaces are used in a test bench. This test bench treats an SPI master and two SPI slaves collectively as devices under test. The test bench provides data to be transmitted by the master and checks to make sure that the slaves receive the correct value from the master. Similarly the test bench provides data for the slaves to transmit and then checks to make sure that data is correctly received by the master.
In the test bench we are using the interfaces and modports the same way as we would use other data types to declare variables.
SPIbus spi(); declares spi as an instance variable for an SPIbus.
SPIctrl tb_ctrlm(); declares tb_ctrlm as an instance variable for an SPIctrl bus.
Notice that you can declare an array of control busses. In this case, SPIctrl tb_ctrls[1:0] declares an array of two SPIctrl busses.
Further down in the test bench, these interface variables are used to connect instances of all of these busses to the SPI master and slave modules.

## Slide 10
Use of interface in test bench
the mapped netlists from design
compiler do not use interfaces as
ports, so one must pass each element
separately as an input or output
Interfaces can be used in test bench expressions and assignments
just as they were in the Master and Slave RTL code.
Notes: We would like to use the same test bench for source and mapped versions of the SPI modules. However, design compiler only gives us a mapped netlist in which each element of the interface is listed as a separate input/output port. Therefore, each element of the interface has to be listed separately in the port map for the mapped version of the device under test.
Further down into the test bench, you will find that we can read or write values on the interface by referring to the interface variable and the name of the element within the interface. In this example, we are taking the value of Rcvd from the slave control interface and assigning it to the variable checkRcvds. This particular always block is part of the test bench code that is used to monitor the outputs of the SPI slaves.

## Slide 11
Use of interface in test bench
Stimulus generation code can assign
values to elements of an interface
just like you would to a variable or
wire that is passed to the device
under test.
Interfaces can be used in assertion expressions
Notes: The upper block of code shows how a Verilog task can be used with an interface to stimulate the inputs of a device under test. In this case, this code generates a sequence of inputs to the master to give it a byte of data to transmit. The control interface tb_ctrlm contains the necessary input signals to the SPI master to do this.
The lower block on this slide shows how one can read values from the control interface to check the correctness of values received by the SPI master.

## Slide 12
Use of interface in simulation – add to waveforms
All interfaces are listed in Questa/Modelsim the same way as modules, processes, etc.
and you add signals to the waveform viewer in the same way.
In the waveform viewer, select the signals you
added, right click, and select “group” to
group the interface signals together.

## Slide 13
Simulation results – assertion messages

## Slide 14
Simulation – Successful Master->Slave transfer
Strobe to master loads 11110001 and slave select[1:0]=“01”
SPI sck and mosi proceed to send data to slave 0. Slave 0 Ready indicates data received.
Data appears on Slave 0 Rcvd.

## Slide 15
Simulation – Failed Master->Slave transfer
Same sequence as successful transfer except that value saved by test bench is deliberately
inverted so that when received value doesn’t match, an error is reported.
See checkMXmit and assertm_fail.

## Slide 16
Simulation – Successful Slave 1 ->Master transfer
Strobe to slave 1 loads value 01001111 to be transmitted next time slave 1 is selected
(i.e., ss = 10) and master cycles sck eight times.

## Slide 17: What you have learned (I hope)
Purpose of System Verilog Interfaces
Basic interface syntax
Use of interface in test bench and design code
Use of interface in simulation and verification
Benefits of interfaces
  Improved modularity of code
  Improved readability of code